## Slide 1: Application Of Brain-Computer Interface In Augmentative And Alternative Communication For Non-Speaking Autistic
A feasibility Study

## Slide 2: Literature Review (2015 to 2022)
BCI studies in autism
  Identification/Classification
    To identify music preferences
    Mental stress during arithmetic tasks
    Emotional state (distress vs non-distress)
    Interest to tasks, engagement level in task, and mental workload
    Social joint attention
  Rehabilitation /training
    Attention
    Social skills
    Social joint attention
    Interpretation of emotional facial expressions
    learning driving

## Slide 3: Method
Participants (N~15; age : +12)
  Formal diagnosis of autism or unspecified neurodevelopmental disability
  Mild intellectual disabilities (ID) or without ID
  Understand speech
  Speak minimally or cannot speak
  No history of epilepsy (risk of photosensitivity)
Measure
  Vineland Adaptive Behavior Scales (VABS)-Third edition

## Slide 4: Paradigm
Selected BCI Modality:
Steady-State Visual Evoked Potentials(SSVEP)
  Benefits:
    No need for training sessions
    No need for overt behavioral responses
    High signal-to-noise ratio (SNR)
    High information transfer rate (ITR)

## Slide 5: Task Design
  A total of 12 pictures (i.e., AAC) will be selected for the task.
  In each trial, 4 pictures will randomly be presented on an LCD monitor in front of the subject and 4 LEDs placed in the top left (1), top right (2), down left (3), and down right (4), of the monitor.
  LEDs flicker with 8, 10, 12, and 15 Hz respectively.
  Subjects try to select the output command (i.e., one of 4 pictures on the monitor) by paying attention to a sound that defines the number of the picture.
  Each session includes 120 trials and each picture will be presented 10 times.
  Each trial time is equal to 7 seconds including 5 seconds picture presentation followed by a 2-second rest black/white screen.
  Overall, 3 sessions will be presented by inserting about a 5-minute break between sessions.

## Slide 7: The SSVEP Shuffle Speller associates a letter (task symbol) with a particular SSVEP response (brain symbol) by placing it near the LED array which stimulates that response. The square and less-than characters represent space and backspace respectively.

## Slide 8: EEG acquisition
  Feasible with 8-channel EEG, using a 10-20 standard system
  Location of EEG electrodes placement: Occipital and Parietal lobs
  The right ear and Fpz will be dedicated to reference and ground electrodes respectively
  Online notch (50 Hz) and bandpass filters (2-100 Hz) will be used
  The frequency sampling frequency in this study is 512 Hz. Synchronization pulses/trigger signals should be recorded simultaneously with EEG signals.

## Slide 9: The location of EEG electrodes

## Slide 10: General block diagram of the experimental setup and data analysis

## Slide 11: SSVEP Evaluation
  Accuracy of classification
    ACC=correct trials/all trials
  Information Transfer Rate (ITR)
    Measured in bits per minute
    This project: Expected one command in 1-2 seconds